## Slide 1
WiFi CSI
Presence Detection
Using Channel State Information from ESP32-C6 & ESP32-C3
Nima Chaharbaghi · Saif Meftah · Florian Milbradt
github.com/nimachaharbaghi/presencedetection
IoT · WiFi Sensing · Real-Time Detection

## Slide 2
What is
CSI?
Channel State
Information
CSI describes how a WiFi signal travels from transmitter to receiver — capturing the amplitude and phase shift of each subcarrier frequency.
~
Beyond RSSI
RSSI gives one number. CSI gives 52–256 complex values per packet — a full fingerprint of the signal path.
⊕
Physics in action
Human bodies absorb 2.4 GHz WiFi at ~60%. Any person in the path measurably distorts the signal.
◎
No extra hardware
Standard 802.11 packets carry CSI. No cameras, no PIR sensors — just the WiFi radio already on the chip.

## Slide 3
Hardware
Both boards under $5 — total hardware cost ~$10
Seeed XIAO ESP32-C6
CSI Receiver
— WiFi 6 (802.11ax)
— RISC-V 160 MHz
— 128 CSI samples/pkt
— ESP-IDF v5.3
~$5
Seeed Studio
XIAO Series
ESP32-C3 DevKit
CSI Transmitter
— WiFi 802.11n
— RISC-V 160 MHz
— 10 packets/sec
— Runs on powerbank
~$4
Generic devkit
AliExpress/Amazon
Total project hardware cost: ~$9 · No soldering required · Plug-and-play USB

## Slide 4
System Architecture
Phone
Hotspot
WiFi AP
Channel 6
ESP32-C3
Transmitter
active_sta
ESP32-C6
Receiver
passive sniffer
Python
Server
WebSocket
csi_server.py
Browser
Dashboard
presence_dashboard
.html
WiFi connection
CSI packets
(raw data)
Serial /dev/
ttyACM0
WebSocket
localhost:8765
1. Transmission
C3 connects to hotspot and fires packets at 10/sec. Each packet triggers a CSI measurement on the receiver.
2. CSI Collection
C6 runs in promiscuous mode on ch.6. For every C3 packet, the WiFi driver captures 128 CSI samples and prints to serial.
3. Presence Detection
Python reads serial, extracts RSSI, computes rolling variance over 50 samples, and compares against a calibrated threshold.

## Slide 5
The Physics
of Detection
WiFi signals travel multiple paths. A human body changes those paths.
60%
of 2.4 GHz absorbed by water in human tissue
52+
subcarriers measured per packet on ESP32-C6
10×
packets per second from the C3 transmitter
<1s
detection latency after calibration
Multipath propagation
C3
TX
C6
RX
direct
person

## Slide 6
Detection Algorithm
01
Filter by MAC
Only packets from the C3's known MAC address are processed. All ambient WiFi traffic is ignored.
02
Rolling window
The last 50 RSSI values are stored in a circular buffer. Smooths noise while staying responsive to real changes.
03
Variance metric
Variance = average squared deviation from the mean. Empty room: low. Person present: higher and fluctuating.
04
Calibration
On startup, 30 seconds of empty-room variance is recorded. Threshold = median + 2 × std deviation + 0.5.
05
Decision
If variance > threshold → person detected. Change in state triggers a WebSocket broadcast and alert sound.
threshold = median(σ²) + 2 × std(σ²) + 0.5

## Slide 7
Hardware & Software Stack
Seeed XIAO ESP32-C6
CSI Receiver · ~$5
— RISC-V 160 MHz
— WiFi 6 (802.11ax)
— USB-Serial/JTAG
— ESP-IDF v5.3
ESP32-C3 DevKit
CSI Transmitter · ~$4
— RISC-V 160 MHz
— WiFi 802.11n
— 10 packets/sec
— ESP-IDF v5.3
Software Stack
ESP-IDF v5.3
Single SDK for both C3 and C6. Provides WiFi driver, CSI API, FreeRTOS.
ESP32-CSI-Tool
Open-source base firmware (StevenMHernandez). Modified for C6 API.
Python + websockets
Reads serial, variance-based detection, broadcasts via WebSocket :8765.
HTML + Web Audio
Single-file dashboard. Live charts, pulsing indicator, beep on detection.

## Slide 8
Live Dashboard
●
Room Empty
RSSI
-57 dBm
Variance
1.8
Threshold
4.2
RSSI signal
Dashboard Features
Live RSSI and variance charts
Pulsing green / red status indicator
Calibration progress bar on startup
Beep sound on detection change
Event log with timestamps
Auto-reconnects on disconnect
Single HTML file — no install needed

## Slide 9
Results & Limitations
What Works Well
✓
Detects entry and exit reliably when someone crosses the signal path
✓
Adaptive calibration adjusts to any room without manual tuning
✓
Dedicated C3 transmitter gives clean, regular 10 Hz signal
✓
Fully passive — no cameras, no PIR, no additional hardware
✓
Sub-second detection latency once calibrated
Current Limitations
×
Stationary people are hard to detect — body must move
×
Sensitive to environmental changes (doors, fans)
×
Single threshold may need re-tuning across rooms
×
RSSI only — full complex CSI values not yet used
×
One detection zone — no localization or counting
Next steps: Use full CSI buffer (128 complex values) instead of RSSI · Apply ML classifier for person counting · Fuse multiple receivers for localization

## Slide 10
Thank You
Questions?
Nima Chaharbaghi · Saif Meftah · Florian Milbradt
github.com/nimachaharbaghi/presencedetection
ESP32-CSI-Tool — github.com/StevenMHernandez/ESP32-CSI-Tool
ESP-IDF v5.3 — github.com/espressif/esp-idf